## Slide 1
Algorithm 2
1
Energy Histogram
Speech and silence segmentation
Frame 25 ms. Hop 10 ms.
Minimum silence duration: 200 ms
Name / Student ID: pending
Notes: Midterm presentation for Algorithm 2. Name / Student ID: pending. The planned presentation lasts about three minutes, followed by a one-minute demonstration. Source: the current assignment and slide submission guidance in Source/assignment.

## Slide 2
Algorithm 2 workflow
2
1. Read WAV with 25/10 ms framing
2. Compute Energy as mean squared amplitude
3. Build Energy histogram and compare W=1..50
4. Hysteresis: merge <200ms gaps, discard <100ms speech
5. Select one W using four test LABs
Train W=1. Global W=20. All W=1..50 tie.
Notes: Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 3
phone_F2: test results
3
MAE 32.50 ms RMSE 39.53 ms
Chart: 
HIGH | 0.0116 | 0.0116
LOW | 0.002515 | 0.002515
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Test LABs tune W. MAE is not independent.
Notes: Sources: outputs/tables/tt2/test_metrics.csv and data/test/phone_F2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0025149672448754727 and HIGH=0.011599505796759687 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=32.499999999999865 ms and RMSE=39.528470752104546 ms. Test LABs tune W. MAE is not independent. Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 4
phone_M2: test results
4
MAE 7.50 ms RMSE 7.91 ms
Chart: 
HIGH | 0.016741 | 0.016741
LOW | 0.002515 | 0.002515
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Test LABs tune W. MAE is not independent.
Notes: Sources: outputs/tables/tt2/test_metrics.csv and data/test/phone_M2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0025149672448754727 and HIGH=0.016741174854225986 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.499999999999951 ms and RMSE=7.905694150420921 ms. Test LABs tune W. MAE is not independent. Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 5
studio_F2: test results
5
MAE 7.51 ms RMSE 7.91 ms
Chart: 
HIGH | 0.012277 | 0.012277
LOW | 0.002515 | 0.002515
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Test LABs tune W. MAE is not independent.
Notes: Sources: outputs/tables/tt2/test_metrics.csv and data/test/studio_F2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0025149672448754727 and HIGH=0.012276785714285716 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.505668934240428 ms and RMSE=7.909282749784279 ms. Test LABs tune W. MAE is not independent. Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 6
studio_M2: test results
6
MAE 7.49 ms RMSE 7.90 ms
Chart: 
HIGH | 0.013021 | 0.013021
LOW | 0.002515 | 0.002515
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Test LABs tune W. MAE is not independent.
Notes: Sources: outputs/tables/tt2/test_metrics.csv and data/test/studio_M2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0025149672448754727 and HIGH=0.013020929394699838 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.494331065759696 ms and RMSE=7.902112055091845 ms. Test LABs tune W. MAE is not independent. Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 7
Error on four test files
7
File | MAE (ms) | RMSE (ms)
phone_F2 | 32.50 | 39.53
phone_M2 | 7.50 | 7.91
studio_F2 | 7.51 | 7.91
studio_M2 | 7.49 | 7.90
Mean MAE: 13.75 ms
Residual noise affects phone_F2.
Test LABs tune W. MAE is not independent.
Notes: Source: outputs/tables/tt2/test_metrics.csv. The summary is the arithmetic mean of the four per-file FINAL endpoint MAEs. Each file has one speech region and two endpoints. MAE averages absolute START/END errors, while RMSE takes the square root of the mean squared errors. Region pairs follow time order. Candidate boundaries do not enter the primary metrics. The assignment does not require a fixed numerical MAE cutoff. Algorithm 2 uses Energy only, as required by the teacher. It does not use spectral centroid or FFT. Energy is the mean squared frame amplitude, E=STE/L, where L is the actual number of samples in that frame. STE is the sum of squared frame samples. The histogram uses 64 bins and smoothing radius 2. The weighted threshold follows the histogram adaptation of Giannakopoulos, while framing follows the assignment at 25 ms / 10 ms. The training proposal is W=1. One global W=20 is then selected using the four test LABs and FINAL region endpoint error. The rule first rejects invalid region counts, then minimizes the worst per-file regret and mean MAE, and retains the previous W on ties. All 50 values W=1..50 tie on these files. The previous W=20 therefore remains selected. These are test-tuned errors and are not independent generalization estimates. Candidate padding is 250 ms. Candidate padding does not set FINAL endpoints. Sources: core/features.py, algorithms/tt2_histogram.py, app/weight_selection.py, outputs/models/tt2.json, outputs/tables/tt2_w_selection/selection.json and summary.csv; Source/references/A method for silence removal and segmentation of speech signals_Giannakopoulos_2014.pdf, pages 1-2. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.