## Slide 1
Algorithm 3
1
Gaussian Distributions
Speech and silence segmentation
Frame 25 ms. Hop 10 ms.
Minimum silence duration: 200 ms
Name / Student ID: pending
Notes: Midterm presentation for Algorithm 3. Name / Student ID: pending. The planned presentation lasts about three minutes, followed by a one-minute demonstration. Source: the current assignment and slide submission guidance in Source/assignment.

## Slide 2
Algorithm 3 workflow
2
1. Read WAV with 25/10 ms framing
2. Compute and normalize STE
3. Estimate training mean and standard deviation
4. Create candidate speech using the Gaussian threshold
5. Hysteresis: merge <200ms gaps, discard <100ms speech
Learned threshold: 0.002877734
Notes: Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 3
phone_F2: test results
3
MAE 27.50 ms RMSE 32.60 ms
Chart: 
HIGH | 0.0043166 | 0.0043166
LOW | 0.0028777 | 0.0028777
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Noise tails can extend speech.
Notes: Sources: outputs/tables/tt3/test_metrics.csv and data/test/phone_F2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0028777336852328582 and HIGH=0.004316600527849287 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=27.499999999999968 ms and RMSE=32.59601202601319 ms. Noise tails can extend speech. Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 4
phone_M2: test results
4
MAE 7.50 ms RMSE 7.91 ms
Chart: 
HIGH | 0.0043166 | 0.0043166
LOW | 0.0028777 | 0.0028777
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Noise tails can extend speech.
Notes: Sources: outputs/tables/tt3/test_metrics.csv and data/test/phone_M2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0028777336852328582 and HIGH=0.004316600527849287 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.499999999999951 ms and RMSE=7.905694150420921 ms. Noise tails can extend speech. Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 5
studio_F2: test results
5
MAE 7.51 ms RMSE 7.91 ms
Chart: 
HIGH | 0.0043166 | 0.0043166
LOW | 0.0028777 | 0.0028777
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Framing and thresholds affect boundary error.
Notes: Sources: outputs/tables/tt3/test_metrics.csv and data/test/studio_F2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0028777336852328582 and HIGH=0.004316600527849287 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.505668934240428 ms and RMSE=7.909282749784279 ms. Framing and thresholds affect boundary error. Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 6
studio_M2: test results
6
MAE 7.49 ms RMSE 7.90 ms
Chart: 
HIGH | 0.0043166 | 0.0043166
LOW | 0.0028777 | 0.0028777
Ground truth boundary 1 | -1 | 1
Ground truth boundary 2 | -1 | 1
FINAL boundary 1 | -1 | 1
FINAL boundary 2 | -1 | 1
Waveform
STE
HIGH
LOW
Ground truth
FINAL
Time (s)
Framing and thresholds affect boundary error.
Notes: Sources: outputs/tables/tt3/test_metrics.csv and data/test/studio_M2.wav, with ground truth from the LAB file of the same name. The gray waveform is downsampled and normalized only for display. Feature extraction uses every original audio sample. Orange STE is normalized by the recording maximum. Red lines mark LAB speech-region endpoints. Blue lines mark the confirmed FINAL endpoints. LOW=0.0028777336852328582 and HIGH=0.004316600527849287 are the actual normalized STE thresholds used for detection. FINAL regions=1. MAE=7.494331065759696 ms and RMSE=7.902112055091845 ms. Framing and thresholds affect boundary error. Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.

## Slide 7
Error on four test files
7
File | MAE (ms) | RMSE (ms)
phone_F2 | 27.50 | 32.60
phone_M2 | 7.50 | 7.91
studio_F2 | 7.51 | 7.91
studio_M2 | 7.49 | 7.90
Mean MAE: 12.50 ms
Gaussian fit depends on training data.
Notes: Source: outputs/tables/tt3/test_metrics.csv. The summary is the arithmetic mean of the four per-file FINAL endpoint MAEs. Each file has one speech region and two endpoints. MAE averages absolute START/END errors, while RMSE takes the square root of the mean squared errors. Region pairs follow time order. Candidate boundaries do not enter the primary metrics. The assignment does not require a fixed numerical MAE cutoff. Algorithm 3 estimates Gaussian distributions from the four training WAV/LAB pairs. The implementation uses population standard deviations and chooses the equal-density crossing between class means. Silence: mean 0.00038711079659476316, standard deviation 0.0007092854827602364, 497 frames. Speech: mean 0.20264889816756282, standard deviation 0.23562613277402947, 794 frames. The saved threshold is 0.0028777336852328582. Test LABs enter evaluation after detection and do not tune this algorithm. Sources: algorithms/tt3_gaussian.py, outputs/models/tt3.json, outputs/tables/training_frames.csv and the current assignment in Source/assignment. Common endpoint refinement uses raw normalized STE. LOW continues speech, and a HIGH frame with the algorithm seed confirms speech. Noise calibration uses training silence only: mean 0.00038711079659476316, population standard deviation 0.0007092854827602364, Q95 0.0012140144555334857, and mean plus three standard deviations 0.0025149672448754727. The system merges internal gaps shorter than 200 ms and discards speech regions shorter than 100 ms. FINAL endpoints follow the union of active frame supports, without fixed final padding. Candidate regions remain diagnostic. Only ordered FINAL START/END pairs enter the primary MAE and RMSE.